| Hampsthwaite Play and Recreation Area – Footbridge project |
| --- |
| Description: A voluntary project to build a 5-metre span timber footbridge, built to North Yorkshire County Council specification, and mounted on Gabion basket abutments to provide pedestrian, wheelchair and pushchair access across Cockhill Beck. |
| Location: Between the Cricket Club and the football field |
| Timings Saturday 14th October 8.00 am until 4.00pm Sunday 15th October 10.00 am until 4.00pm Saturday 21st October 8.00 am until 4.00pm |
| Risk Assessment methodology: Step 1. Identify the Hazard. Step 2. Identify “Who may be harmed? Children General public Volunteers (site workers) Step 3. Determine the Risk. Likelihood (LHD) Very low - Definitely will not happen Low - Unlikely to happen Medium - Moderate chance of accident happening High - Quite likely to happen Very high - Likelihood is it will happen Consequence (CON) Very low - Injury very insignificant i.e. splinters Low - Injury fairly minor i.e. minor cut, graze, bruising Medium - Injury would stop casualty continuing with task. High - Serious injury requiring medical assistance i.e. broken bones, deep cut Very high - Very serious injury or possible fatality Step 4. Implement Control Measures. Residual Risk (RR) - the level of risk that remains after implementing control measures. Very low - Minimal risk, control measure more then necessary Low - Control measures satisfactory Medium Control - measures adequate High Control - measure requires constant supervision. Re-assess situation Very high - Control measures inadequate. Stop activity Step 5. Review Process. Risk assessments will be reviewed when it is suspected that the assessment is no longer valid or there has been a significant change. As a minimum, they will be thoroughly reviewed at the start of any new voluntary project or annually for on-going projects and activities. |
| Risk Assessment: |
| Task: | Hazard(s): | Who’s at risk: | Risk Level: (LHD) | Risk Level: (CON) | Precautions and Control Measures required: (State existing measures if adequate) | Further Action Necessary: | Risk Level: (RR) |
| Deliver materials and excavation equipment to site | Intermingling of pedestrians, plant and machinery | Saturday morning football teams General public | Low | Medium | Deliver all materials, plant and machinery to site outside school hours and to arrive before the start of Saturday morning football matches. | Community Police Officer on duty Saturday morning to direct spectators to football match away from site. | Low |
| Excavate stream bed | Proximity of people to mechanical excavator. Excavator tipping into stream | Site workers Excavator operator | Low | Medium | Excavator to be operated only by suitably qualified or experienced personnel Authorised site workers to wear high visibility clothing and hard hats. No unauthorised people, including children, to be within 50 feet of the excavator when in operation. | Outer perimeter of site to be marshalled by volunteers when excavator is in operation | Low |
| Assemble Gabion baskets | Finger cuts on sharp wire ends | Site workers | Low | Very Low | Wear gloves Bend over any sharp ends | none | Low |
| Hand fill baskets with stone | Fingers trapped by stones Back strain | Site workers | Low | Low | Wear gloves Use pinch bars Two or more people to lift stones greater than 25 Kg. | none | Low |
| Landscape immediate surroundings | Fingers trapped by stones Back strain Toes crushed | Site workers | Low | Low | Wear gloves and stout footwear – safety boots worn by those handling the largest stones Use pinch bars Two or more people to lift stones greater than 25 Kg. | none | Low |
| Remove equipment from site | Intermingling of pedestrians, plant and machinery | General public | Low | Medium | Remove machinery from site at a time when there is no activity or event at or near the Cricket Club | none | Low |
| Manufacture timber bridge components | Cuts from sharp edge tools | Site workers | Low | High | Components manufactured off-site in controlled workshop conditions by qualified wood machinists. | none | Low |
| Assemble bridge components on site | Lifting and positioning heavy beams Splinters Finger traps Back strain Use of power tools | Site workers | Low | Low | Main 12” x 8” beams to be constructed by bolting together two 12” x 4” beams. Beams positioned by minimum of three site workers Wear gloves Power tools used only by suitably qualified or experienced personnel | Use battery operated power tools on site | Low |
| Method statement: All materials, plant and equipment will be delivered to the works site between 3.00 Friday 13th Oct and 8.30 am Saturday 14th October. Volunteers should not arrive before 9.00am and should endeavour to park their cars as far away from the Cricket Club as is possible to avoid further congestion – if there is any equipment to deliver, then this should be done before 8.30am Saturday 14th October. Each volunteer will be responsible for providing their own suitable clothing, personal protection and footwear bearing in mind the following: When the digger is operating, only nominated authorised personnel can be within the perimeter of the building works. The remaining volunteers should position themselves around the perimeter and help marshal the works area to prevent unauthorised access by children or others. No one can be within 50 feet of the digger when in operation without hardhat and high visibility clothing. The work following excavation will comprise mainly filling Gabion (wire mesh) baskets with stone to form bridge abutments. The baskets will be assembled and positioned under the direction of Martin Weston (Construction Marine). Personal protection for those wishing to be engaged in filling the baskets should include: stout footwear (preferably safety boots), gloves, hardhat, high visibility clothing. Some volunteers will be engaged gathering additional rocks from the bed and banks of the beck outwith the immediate works area. They should have as a minimum, stout footwear and gloves. Gloves and pinch bars should be used at all times when there is any risk of finger trapping. Rocks heavier than 20 kilograms (or football size) should be handled by two or more volunteers. Only volunteers with safety boots will be authorised to position any lager stones required for final landscaping. Harrogate Timber will do the manufacture of components for the timber bridge itself off-site with final fitting by Geoff Howard in workshop conditions. Components will be delivered to site before 8.30am on Saturday 21st October and assembled using battery powered hand tools where these are required – i.e. drills Geoff Howard will be responsible for authorising personnel and assigning tasks. He will also be the contact in case of accident and will be carrying a mobile phone with access to local medical help if required. The Parish Council’s Public Liability insurance to a maximum of £5 million covers this voluntary project. |
| Geoff Howard 11th October 2006 Review date (if needed) October 2007 |